GETTING STARTED

As we all know from experience, getting started is sometimes the most difficult part of any task. Fortunately, most of the items on the maintenance checklist are neither time consuming nor difficult. In addition to the information provided in this newsletter, there are excellent reference books at your local library or home improvement store on the subject of homecare and maintenance.

STEP 1: Assemble the required, proper tools and supplies. Being prepared before you begin will save time later!

STEP2: Get organized and plan your approach to accomplishing the tasks at hand.

CAULKING MAINTENANCE

Most building materials are subject to varying degrees of shrinkage and settlement, as well as normal expansion and contraction, caused by changes in climate and humidity.

Frequent inspection and maintenance of the caulking on the exterior of your home and in the tubs, sinks and showers inside your home will protect the finishes surrounding these typically wet areas. The following is a suggested checklist of some of the areas of your home that require caulking and subsequent maintenance:

CAULKING MAINTENANCE CHECKLIST

| INTERIOR: | __bathtubs | __vanities tile |
| --- | --- | --- |
|  | __showers | __trim |
|  | __sinks | __drywall |
|  | __countertops |  |
| EXTERIOR: | __windows | __siding/brick |
|  | __doors & sidelights | __flashings/copper roofs |
|  | __wood trim | __porches/columns |
|  | __wood bay & box windows | __vents |
|  | __garage doors/ |  |

Time and weather will dry and shrink caulking so that it no longer provides a good seal. Normal expansion, contraction and settlement will cause caulking to separate. As part of your routine maintenance, check the caulking in the above areas periodically and make timely repairs as needed.

Caulking compounds and dispenser guns are available at local hardware stores. Read the manufacturer's instructions carefully to be certain that you select an appropriate caulk for the intended purpose. As a homeowner, you should choose caulking wisely and apply it properly and consistently. Wise use of caulk will protect your home from damaging elements and maintain its beauty for years to come.

AVOID ELECTRICAL HAZARDS

If a GFI receptacle is not functioning press the Reset button on the wall plate to restore proper operation. If that does not work check and reset the circuit breaker in the panel box first, then press the GFI Reset button. If the outlet still fails it may indicate a short in the appliance. If other appliances will not operate in the outlet an electrician should be contacted and the GFI replaced.

FIRE SAFETY

Smoke and carbon monoxide detectors are perhaps the most important components of your electrical system. While they are wired directly into your home's electrical system, most models include a battery back-up. A chirping sound indicates that the battery is weak and needs to be replaced. Safeguard your family and guests by replacing all your smoke and carbon monoxide detector batteries ANNUALLY.

Test your smoke and carbon monoxide detectors regularly by pushing the test button on each unit. The alarm should sound. If it does not, call for service immediately.

A FAMILY FIRE PLAN:

Every family should develop and periodically review their fire plan. How do you all get out safely in the event of a fire? Where do you meet outside the home? You may want to contact your local fire department for general fire safety information for assistance.

|  | FALL/WINTER MAINTENANCE CHECKLIST |
| --- | --- |
|  | REGULARLY | Clean/maintain floor coverings per manufacturers' recommendations. | INTERIOR |
|  | REGULARLY | Maintain appliances, mechanical, plumbing, and electrical equipment per manufacturers' instructions. | INTERIOR |
|  | MONTHLY | Change or clean all furnace/air conditioning filters. | INTERIOR |
|  | MONTHLY | Clean and test smoke detectors and CO detectors. Test smoke detectors by pushing round button on face of detector (should be labeled "test"). Change batteries as necessary. | INTERIOR |
|  | MONTHLY | Test and reset GFCI breakers/outlets | EXT/INT |
|  | FALL | Check exterior caulking, and recaulk as required. | EXTERIOR |
|  | FALL | Check exterior paint and stain surfaces and refinish as needed. | EXTERIOR |
|  | FALL | Adjust exterior doors/weatherstripping as needed to close/seal properly | EXTERIOR |
|  | FALL | Check gutters for debris and clean as required. Confirm that downspouts and splash blocks drain away from the home. | EXTERIOR |
|  | FALL | Fill in settlement of backfill soil where needed to maintain proper drainage. | EXTERIOR |
|  | FALL | Winterize sprinkler system | EXTERIOR |
|  | FALL | Winterize exterior hose bibs and disconnect hoses | EXTERIOR |
|  | FALL | Apply driveway sealant (Fall/Spring - Season Optional) | EXTERIOR |
|  | FALL | Seal wooden decks (Fall/Spring - Season Optional) | EXTERIOR |
|  | FALL | Clean up lawn, and administer seasonal applications per lawn care plan. | EXTERIOR |
|  | FALL | Wash windows and screens, clean weep holes, and lubricate tracks. | EXT/INT |
|  | FALL | Verify sump pump operation. Keep drainage channels/discharge free of obstructions. | INTERIOR |
|  | FALL | Start and operate heating system and provide service as required. | INTERIOR |
|  | FALL | Service and startup humidifier per manufacturer's instructions. | INTERIOR |
|  | FALL | Check condensation drain/pump for humidifier - clean/maintain as required. | INTERIOR |
|  | FALL | Adjust HVAC registers. Confirm that supplies and returns are clear of furniture, etc. | INTERIOR |
|  | FALL | Adjust doors/hardware to accommodate settlement/climatic conditions. | INTERIOR |
|  | FALL | Check overhead garage doors. tighten bolts as needed, and lubricate springs/tracks. | INTERIOR |
|  | WINTER | Check interior caulking, and recaulk as required. | INTERIOR |
|  | WINTER | Inspect grout around floor and wall tile and touch-up as necessary. | INTERIOR |
|  | WINTER | Inspect for shrinkage maintenance such as minor drywall cracks, nail pops, and separations of wood trim. Repair as needed | INTERIOR |
|  | WINTER | Remove snow/ice from sidewalks and driveway surfaces. | EXTERIOR |
|  | WINTER | Avoid using rock salt/or damaging de-icing agents | EXTERIOR |
|  | PERIODIC | Spackle and paint as required due to normal living activity | INTERIOR |
|  | PERIODIC | Recaulk and repaint minor separations in wood trim (due to natural shrinkage/settlement) as required. | INTERIOR |
|  | PERIODIC | Recaulk and repaint faded/deteriorated exterior trim/doors/shutters (due to natural effects of sun weather, etc.) as required. | EXTERIOR |
|  | PERIODIC | Drain water heater(s) per manufacturers' instructions. Your local water quality determines frequency needed. | INTERIOR |
|  | PERIODIC | Have the water tested if your home has a private well. | EXTERIOR |
|  | PERIODIC | Service fireplace/flue by professional. | INT/EXT |

SPRING/SUMMER MAINTENANCE CHECKLIST

| √ | SEASON | TASK | INTERIOR EXTERIOR |
| --- | --- | --- | --- |
|  | REGULARLY | Clean/maintain floor coverings per manufacturers' recommendations. | INTERIOR |
|  | REGULARLY | Maintain appliances, mechanical, plumbing, and electrical equipment per manufacturers' instructions. | INTERIOR |
|  | MONTHLY | Change or clean all furnace/air conditioning filters. | INTERIOR |
|  | MONTHLY | Clean and test smoke detectors and/or CO detectors. Test smoke detectors by pushing round button on face of detector (should be labeled "test"). Change batteries as necessary | INTERIOR |
|  | MONTHLY | Test and reset GFCI breakers/outlets | INTERIOR |
|  | SPRING | WHERE APPLICABLE -Check all sump pumps to ensure that they are operational where applicable and remove any existing debris. | INTERIOR |
|  | SPRING | Open shut-off valves for exterior hose bibs. | INTERIOR |
|  | SPRING | Inspect for shrinkage such as minor drywall cracks, nail pops, and separations of wood trim. Repair as needed. | INTERIOR |
|  | SPRING | Readjust doors/hardware to accommodate settlement/climatic conditions. | INTERIOR |
|  | SPRING | Check overhead garage doors, tighten bolts as needed, and lubricate springs/tracks | INTERIOR |
|  | SPRING | Check and operate air-conditioning system. | INTERIOR |
|  | SPRING | If applicable turn humidifier(s) off and shut off water supply. | INTERIOR |
|  | SPRING | Check condensation drain/pump for air conditioning system. Clean/maintain as required. | INTERIOR |
|  | SPRING | Make sure that all air registers and returns are clear of furniture and/or draperies. You may find it necessary to vacuum all air returns to remove dirt and dust. | INTERIOR |
|  | SPRING | Ensure air-conditioning compressor is level and clear of obstructions and debris. | INTERIOR |
|  | SPRING | Check exterior caulking and recaulk as required. | EXTERIOR |
|  | SPRING | Check exterior paint and stain surfaces (especially stained doors). Refinish as needed. | EXTERIOR |
|  | SPRING | Check gutters for debris. Confirm that down spouts & splash blocks drain away from the home. | EXTERIOR |
|  | SPRING | Inspect the ground surrounding your home for any soil erosion and positive drainage. If any erosion exists it is your responsibility to restore the yard to the original grade. | EXTERIOR |
|  | SPRING | Wash windows and screens, clean weep holes, and lubricate tracks | EXTERIOR |
|  | SPRING | All areaways and window wells should be clear of dirt and leaves. It may also be neces- sary to flush water through your drain to ensure water is flowing freely. |  |
|  | SPRING | Seal wooden decks/stairs annually (Spring/Fall- season optional) | EXTERIOR |
|  | SPRING | Start-up and adjust sprinkler system. Test system for leaks or broken pipes. | EXTERIOR |
|  | SPRING | Clean up lawn, and administer seasonal applications per lawn care plan. | EXTERIOR |
|  | SPRING | Adjust exterior doors/weather stripping as needed to close/seal properly | EXTERIOR |
|  | SUMMER | Check interior caulking, and recaulk as required. | INTERIOR |
|  | SUMMER | Inspect grout around floor and wall tile and touch-up as necessary. | INTERIOR |
|  | SUMMER | Check sprinkler head adjustments regularly. | EXTERIOR |
|  | PERIODIC | Spackle and paint as required due to normal living activity | INTERIOR |
|  | PERIODIC | Recaulk and repaint minor separations in wood trim (due to natural shrinkage/settlement) as required. | INTERIOR |
|  | PERIODIC | Recaulk and repaint faded/deteriorated exterior trim/doors/shutters (due to natural effects of sun weather, etc.) as required. | EXTERIOR |
|  | PERIODIC | Have the water tested if your home has a private well. | EXTERIOR |
|  | PERIODIC | If applicable inspect and clean out all weep holes in brick face | EXTERIOR |